## PHASE-1 Pad Ring and Floor Plan View

## Pad List: (yellow means mandatory, green means advisory)

| Section 1 – Temperature sensor and Analog bias for pixels |
| --- |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 1 | 1 | TEMP | temperature sensor | DIRECTPAD | direct pad |
| 2 | 2 | gnda! | analog ground | AGND3ALLP | power |
| 3 | 3 | gnda!_Prob (*) | analog ground | AGND3ALLP | power |
| 4 | 4 | v_clp! | clamping voltage for pixels | DIRECTPAD | power |
| 5 | 5 | v_clp!_Prob (*) | clamping voltage for pixels | DIRECTPAD | power |
| 6 | 6 | vdda!_Prob (*) | analog power | AVDD3ALLP | power |
| 7 | 7 | vdda! | analog power | AVDD3ALLP | power |
| Section 2 – JTAG control and Digital Output Channel 3 |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 8 | 8 | vdd!_Prob (*) | digital power | VDD3ALLP | power |
| 9 | 9 | vdd! | digital power | VDD3ALLP | power |
| 10 | 10 | TCK | JTAG clock | ICCK2P | DI-clockin |
| 11 | --- | TCK Prob (*) | JTAG clock ?? | ProbePad |  |
| 12 | 11 | TDI | JTAG data input | ICUP | DI-pullup |
| 13 | --- | TDI Prob (*) | JTAG data input ?? | ProbePad |  |
| 14 | 12 | TMS | JTAG mode state | ICUP | DI-pullup |
| 15 | --- | TMS Prob (*) | JTAG mode state ?? | ProbePad |  |
| 16 | 13 | TDO | JTAG data output | BT4P | DO 3-state, 4mA |
| 17 | --- | TDO Prob (*) | JTAG data output ?? | ProbePad | probe |
| 18 | 14 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| 19 | 15 | gnd! | digital ground | GND3ALLP | power |
| 20 | 16 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| 21 | 17 | OUT3_CMOS<3> | data output slow speed channel 3, stream 3 | BU4P | DO 3-state, 4mA |
| 22 | 18 | gnd! | digital ground | GND3ALLP | power |
| 23 | 19 | OUT3_CMOS<2> | data output slow speed channel 3, stream 2 | BU4P | DO 3-state, 4mA |
| 24 | 20 | gnd! | digital ground | GND3ALLP | power |
| 25 | --- | OUT_LVDSp<3> Prob (*) | data output fast speed, channel 3 ?? | probePad | probe |
| 26 | 21 | OUT_LVDSp<3> | data output fast speed, channel 3 | LVDS-TX | DO LVDS |
| 27 | 22 | OUT_LVDSn<3> | data output fast speed, channel 3 | LVDS-TX | DO LVDS |
| 28 | --- | OUT_LVDSn<3> Prob (*) | data output fast speed, channel 3 ?? | ProbePad | probe |
| 29 | 23 | vdd! | digital power | VDD3ALLP | power |
| 30 | 24 | OUT3_CMOS<1> | data output slow speed channel 3, stream 1 | BU4P | DO 3-state, 4mA |
| 31 | 25 | vdd! | digital power | VDD3ALLP | power |
| 32 | 26 | OUT3_CMOS<0> | data output slow speed channel 3, stream 0 | BU4P | DO 3-state, 4mA |
| 33 | 27 | vdd!_Prob (*) | digital power | VDD3ALLP | power |

| Section 3 – Analog bias and DACs |
| --- |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 34 | 28 | gnda!_Prob (*) | analog ground | AGND3ALLP | Power |
| 35 | 29 | gnda! | analog ground | AGND3ALLP | Power |
| 36 | 30 | vdda! | analog power | AVDD3ALLP | Power |
| 37 | 31 | vdda! | analog power | AVDD3ALLP | Power |
| 38 | 32 | vdda! | analog power | AVDD3ALLP | Power |
| 39 | 33 | vdda!_Prob (*) | analog power | AVDD3ALLP | Power |
| 40 | 34 | gnda! | analog ground | AGND3ALLP | Power |
| 41 | 35 | Itest |  | APRIOP | Power |
| 42 | --- | Itest Prob (*) | Itest ?? | probePad | Probe |
| 43 | 36 | gnda! | analog ground | AGND3ALLP | Power |
| 44 | 37 | VCLPDIS | discriminator clamping, external injection | DIRECTPAD | direct pad |
| 45 | 38 | gnda! | analog ground | AGND3ALLP | Power |
| 46 | 39 | VKIMO | circuit monitoring | APRIOP | AIO 0 Ohm |
| 47 | 40 | gnda! | analog ground | AGND3ALLP | Power |
| 48 | 41 | VCLPDIS | discriminator clamping, external injection | DIRECTPAD | direct pad |
| 49 | 42 | gnda! | analog ground | AGND3ALLP | Power |
| 50 | 43 | vdda!_Prob (*) | analog power | AVDD3ALLP | Power |
| 51 | 44 | vdda! | analog power | AVDD3ALLP | Power |
| 52 | 45 | vdda! | analog power | AVDD3ALLP | Power |
| 53 | 46 | vdda! | analog power | AVDD3ALLP | Power |
| 54 | 47 | gnda! | analog ground | AGND3ALLP | Power |
| 55 | 48 | gnda!_Prob (*) | analog ground | AGND3ALLP | Power |
| Section 4 – Synchronization and Digital Output Channel 2 |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 56 | 49 | SPEAK | activate readout marker and clock | ICPD | DI-pulldown |
| 57 | --- | SPEAK Prob (*) | activate readout marker and clock ?? | probePad | Probe |
| 58 | 50 | vdd!_Prob (*) | digital power | VDD3ALLP | Power |
| 59 | 51 | START | synchronize the outputs | ICPD | DI-pulldown |
| 60 | --- | START Prob (*) | synchronize the outputs ?? | probePad | Probe |
| 61 | 52 | vdd! | digital power | VDD3ALLP | Power |
| 62 | --- | MK_CLKD_p Prob (*) | marker and clock for digital data ?? | probePad | Probe |
| 63 | 53 | MK_CLKD_p | marker and clock for digital data | LVDS-TX | DO LVDS |
| 64 | 54 | MK_CLKD_n | marker and clock for digital data | LVDS-TX | DO LVDS |
| 65 | --- | MK_CLKD_n Prob (*) | marker and clock for digital data ?? | probePad | Probe |
| 66 | 55 | gnd! | digital ground | GND3ALLP | Power |
| 67 | 56 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| 68 | 57 | OUT2_CMOS<3> | data output slow speed channel 2, stream 3 | BU4P | DO 3-state, 4mA |
| 69 | 58 | gnd! | digital ground | GND3ALLP | power |
| 70 | 59 | OUT2_CMOS<2> | data output slow speed channel 2, stream 2 | BU4P | DO 3-state, 4mA |
| 71 | 60 | gnd! | digital ground | GND3ALLP | power |
| 72 | --- | OUT_LVDSp<2> Prob (*) | data output fast speed, channel 2 ?? | probePad | probe |
| 73 | 61 | OUT_LVDSp<2> | data output fast speed, channel 2 | LVDS-TX | DO LVDS |
| 74 | 62 | OUT_LVDSn<2> | data output fast speed, channel 2 | LVDS-TX | DO LVDS |
| 75 | --- | OUT_LVDSn<2> Prob (*) | data output fast speed, channel 2 ?? | probePad | probe |
| 76 | 63 | vdd! | digital power | VDD3ALLP | power |
| 77 | 64 | OUT2_CMOS<1> | data output slow speed channel 2, stream 1 | BU4P | DO 3-state, 4mA |
| 78 | 65 | vdd! | digital power | VDD3ALLP | power |
| 79 | 66 | OUT2_CMOS<0> | data output slow speed channel 2, stream 0 | BU4P | DO 3-state, 4mA |
| 80 | 67 | vdd!_Prob (*) | digital power | VDD3ALLP | power |
| 81 | 68 | vdd! | digital power | VDD3ALLP | power |
| 82 | --- | CLKD_p Prob (*) | readout clock for digital data ?? | probePad | probe |
| 83 | 69 | CLKD_p | readout clock for digital data | LVDS-TX | DO LVDS |
| 84 | 70 | CLKD_n | readout clock for digital data | LVDS-TX | DO LVDS |
| 85 | --- | CLKD_n Prob (*) | readout clock for digital data ?? | probePad | probe |
| 86 | 71 | gnd! | digital ground |  | power |
| 87 | 72 | RSTB | asynchronous reset, active low | ISUP | DI-pullup, schmitt |
| 88 | --- | RSTB Prob (*) | asynchronous reset, active low ?? | probePad | probe |
| 89 | 73 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| Section 5 – Analog bias for pixels |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 90 | 74 | gnda! | analog ground | AGND3ALLP | power |
| 91 | 75 | v_clp! | clamping voltage for pixels | DIRECTPAD | direct pad |
| 92 | 76 | vdda! | analog power | AVDD3ALLP | power |
| Section 6 – Master clock (LVDS) |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 93 | 77 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| 94 | 78 | gnd! | digital ground | GND3ALLP | power |
| 95 | --- | CKR_p Prob (*) | master clock, LVDS compatible ?? | probePad | probe |
| 96 | 79 | CKR_p | master clock, LVDS compatible | LVDS-RX | DI LVDS |
| 97 | 80 | CKR_n | master clock, LVDS compatible | LVDS-RX | DI LVDS |
| 98 | --- | CKR_n Prob (*) | master clock, LVDS compatible ?? | probePad | probe |
| 99 | 81 | vdd! | digital power | VDD3ALLP | power |
| 100 | 82 | vdd!_Prob (*) | digital power | VDD3ALLP | power |
| Section 7 – Master clock (PLL synthesizer) |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 101 | 83 | VDDD | digital power | VDD3ALLP | power |
| 102 | 84 | GNDD | digital ground | GND3ALLP | power |
| 103 | 85 | REFCLK | master clock, low frequency | ICCK2P | DI clockin |
| 104 | 86 | GNDA | analog ground | AGND3ALLP | power |
| 105 | 87 | VDDA | analog power | AVDD3ALLP | power |
| 106 | 88 | GNDV | analog ground | AGND3ALLP | power |
| Section 8 – Analog bias for pixels |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 107 | 89 | gnda! | analog ground | AGND3ALLP | power |
| 108 | 90 | v_clp! | clamping voltage for pixels | DIRECTPAD | direct pad |
| 109 | 91 | vdda! | analog power | AVDD3ALLP | power |
| Section 9 –Digital Output Channel 1 and Readout clock |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 110 | 92 | CKCMOS | master clock, CMOS compatible | ICCK2P | DI clockin |
| 111 | --- | CKCMOS Prob (*) | master clock, CMOS compatible ?? | probePad | probe |
| 112 | 93 | vdd! | digital power | VDD3ALLP | power |
| 113 | 94 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| 114 | 95 | OUT1_CMOS<3> | data output slow speed channel 1, stream 3 | BU4P | DO 3-state, 4mA |
| 115 | 96 | gnd! | digital ground | GND3ALLP | power |
| 116 | 97 | OUT1_CMOS<2> | data output slow speed channel 1, stream 2 | BU4P | DO 3-state, 4mA |
| 117 | 98 | gnd! | digital ground | GND3ALLP | power |
| 118 |  | OUT_LVDSp<1> Prob (*) | data output fast speed, channel 1 ?? | probePad | probe |
| 119 | 99 | OUT_LVDSp<1> | data output fast speed, channel 1 | LVDS-TX | DO LVDS |
| 120 | 100 | OUT_LVDSn<1> | data output fast speed, channel 1 | LVDS-TX | DO LVDS |
| 121 | --- | OUT_LVDSn<1> Prob (*) | data output fast speed, channel 1 ?? | ProbePad | probe |
| 122 | 101 | vdd! | digital power | VDD3ALLP | power |
| 123 | 102 | OUT1_CMOS<1> | data output slow speed channel 1, stream 1 | BU4P | DO 3-state, 4mA |
| 124 | 103 | vdd! | digital power | VDD3ALLP | power |
| 125 | 104 | OUT1_CMOS<0> | data output slow speed channel 1, stream 0 | BU4P | DO 3-state, 4mA |
| 126 | 105 | vdd!_Prob (*) | digital power | VDD3ALLP | power |
| 127 | 106 | CLKA | readout clock for analog data | BT4P | DO 3-state, 4mA |
| 128 | --- | CLKA Prob (*) | readout clock for analog data ?? | probePad | probe |
| 129 | 107 | MK_CLKA | marker and clock for analog data | BT4P | DO 3-state, 4mA |
| 130 | --- | MK_CLKA Prob (*) | marker and clock for analog data ?? | probePad | probe |
| 131 | 108 | gnda!_Prob (*) | digital ground | GND3ALLP | power |
| 132 | 109 | tst1pad | readout test pad 1 | BT2P | DO 3-state, 2mA |
| 133 | --- | tst1pad Prob (*) | readout test pad 1 ?? | probePad | probe |
| 134 | 110 | vdd!_Prob (*) | digital power | VDD3ALLP | power |
| 135 | 111 | tst2pad | readout test pad 2 | BT2P | DO 3-state, 2mA |
| 136 | --- | tst2pad Prob (*) | readout test pad 2 ?? | probePad | probe |
| 137 | 112 | gnd! | digital ground | GND3ALLP | power |
| Section 10 – Analog test for discriminator |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 138 | 113 | gnda!_Prob (*) | analog ground | AGND3ALLP | power |
| 139 | 114 | gnda! | analog ground | AGND3ALLP | power |
| 140 | 115 | vdda! | analog power | AVDD3ALLP | power |
| 141 | 116 | vdda! | analog power | AVDD3ALLP | power |
| 142 | 117 | vdda! | analog power | AVDD3ALLP | power |
| 143 | 118 | vdda! | analog power | AVDD3ALLP | power |
| 144 | 119 | vdda!_Prob (*) | analog power | AVDD3ALLP | power |
| 145 | 120 | gnda! | analog ground | AGND3ALLP | power |
| 146 | 121 | Vtst1 | vtest1, external injection | APRIOP | AIO 0 Ohm |
| 147 | 122 | gnda! | analog ground | AGND3ALLP | power |
| 148 | 123 | Vtst2 | vtest2, external injection | APRIOP | AIO 0 Ohm |
| 149 | 124 | gnda! | analog ground | AGND3ALLP | power |
| 150 | 125 | Vref2 | vref2, external injection | APRIOP | AIO 0 Ohm |
| 151 | 126 | gnda! | analog ground | AGND3ALLP | power |
| 152 | 127 | Vref1 | vref2, external injection | APRIOP | AIO 0 Ohm |
| 153 | 128 | gnda! | analog ground | AGND3ALLP | power |
| 154 | 129 | vdda!_Prob (*) | analog power | AVDD3ALLP | power |
| 155 | 130 | vdda! | analog power | AVDD3ALLP | power |
| 156 | 131 | vdda! | analog power | AVDD3ALLP | power |
| 157 | 132 | vdda! | analog power | AVDD3ALLP | power |
| 158 | 133 | gnda! | analog ground | AGND3ALLP | power |
| 159 | 134 | gnda!_Prob (*) | analog ground | AGND3ALLP | power |
| Section 11 – Digital Output Channel 0 |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 160 | 135 | gnd!_Prob (*) | digital ground | GND3ALLP | power |
| 161 | 136 | OUT0_CMOS<3> | data output slow speed channel 0, stream 3 | BU4P | DO 3-state, 4mA |
| 162 | 137 | gnd! | digital ground | GND3ALLP | power |
| 163 | 138 | OUT0_CMOS<2> | data output slow speed channel 0, stream 2 | BU4P | DO 3-state, 4mA |
| 164 | 139 | gnd! | digital ground | GND3ALLP | power |
| 165 | --- | OUT_LVDSp<0> Prob (*) | data output fast speed, channel 0 ?? | probePad | probe |
| 166 | 140 | OUT_LVDSp<0> | data output fast speed, channel 0 | LVDS-TX | DO LVDS |
| 167 | 141 | OUT_LVDSn<0> | data output fast speed, channel 0 | LVDS-TX | DO LVDS |
| 168 | --- | OUT_LVDSn<0> Prob (*) | data output fast speed, channel 0 ?? | ProbePad | probe |
| 169 | 142 | vdd! | digital power | VDD3ALLP | power |
| 170 | 143 | OUT0_CMOS<1> | data output slow speed channel 0, stream 1 | BU4P | DO 3-state, 4mA |
| 171 | 144 | vdd! | digital power | VDD3ALLP | power |
| 172 | 145 | OUT0_CMOS<0> | data output slow speed channel 0, stream 0 | BU4P | DO 3-state, 4mA |
| 173 | 146 | vdd!_Prob (*) | digital power | VDD3ALLP | power |
| Section 12 – Test: PLL synthesizer |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 174 | 147 | RESET | asynchronous reset, active low | ISUP | DI-pullup, schmitt |
| 175 | 148 | VDDD | digital power | VDD3ALLP | power |
| 176 | 149 | REFCLK | master clock, CMOS compatible | ICCK2P | DI clockin |
| 177 | 150 | FB | feedback | BU4P | DO 3-state, 4mA |
| 178 | 151 | GNDD | digital ground | GND3ALLP | power |
| 179 | 152 | OUTCLOCKp | synthesized clock | LVDS-TX | DO LVDS |
| 180 | 153 | OUTCLOCKn | synthesized clock | LVDS-TX | DO LVDS |
| 181 | 154 | VDDAI | analog power | AVDD3ALLP | power |
| 182 | 155 | GNDA | analog ground | AGND3ALLP | power |
| 183 | 156 | CTL | voltage control for oscillator | APRIOP | AIO 0 Ohm |
| 184 | 157 | VDDAO | analog power | AVDD3ALLP | power |
| 185 | 158 | VDDVO | analog power | AVDD3ALLP | power |
| 186 | 159 | VDDVI | analog power | AVDD3ALLP | power |
| 187 | 160 | GNDV | analog ground | AGND3ALLP | power |
| Section 13 – Analog bias for pixels |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 188 | 161 | v_clp! | clamping voltage for pixels | DIRECTPAD | direct pad |
| 189 | 162 | v_clp!_Prob (*) | clamping voltage for pixels | DIRECTPAD | direct pad |
| Section 14 – Test : Analog outputs from the matrix |
| Phy Pad | IPHCPad | Name | Description | Cell | Type |
| 190 | --- | gnd!_test Prob (*) | analog ground ?? | g_pad | test pad |
| 191 | 163 | gnd!_test | analog ground | g_pad | test pad |
| 192 | --- | vdda!_test Prob (*) | analog power ?? | g_pad | test pad |
| 193 | 164 | vdda!_test | analog power | g_pad | test pad |
| 194 | --- | Out<0> Prob (*) | analog output<0> test mode ?? | g_pad | test pad |
| 195 | 165 | Out<0> | analog output<0> test mode | g_pad | test pad |
| 196 | --- | Out<1> Prob (*) | analog output<1> test mode ?? | g_pad | test pad |
| 197 | 166 | Out<1> | analog output<1> test mode | g_pad | test pad |
| 198 | --- | Out<2> Prob (*) | analog output<2> test mode ?? | g_pad | test pad |
| 199 | 167 | Out<2> | analog output<2> test mode | g_pad | test pad |
| 200 | --- | Out<3> Prob (*) | analog output<3> test mode ?? | g_pad | test pad |
| 201 | 168 | Out<3> | analog output<3> test mode | g_pad | test pad |
| 202 | --- | Out<4> Prob (*) | analog output<4> test mode ?? | g_pad | test pad |
| 203 | 169 | Out<4> | analog output<4> test mode | g_pad | test pad |
| 204 | --- | Out<5> Prob (*) | analog output<5> test mode ?? | g_pad | test pad |
| 205 | 170 | Out<5> | analog output<5> test mode | g_pad | test pad |
| 206 | --- | Out<6> Prob (*) | analog output<6> test mode ?? | g_pad | test pad |
| 207 | 171 | Out<6> | analog output<6> test mode | g_pad | test pad |
| 208 | --- | Out<7> Prob (*) | analog output<7> test mode ?? | g_pad | test pad |
| 209 | 172 | Out<7> | analog output<7> test mode | g_pad | test pad |

(*) Probe pads are used only for test purpose and should not be bonded

# Text boxes

Figure 1 – The pad layout of PHASE-1. Only the top edge and the bottom edge are visible. The pads used for the test with a probe station are also drawn but not named because they reproduce the functionality of the adjacent pad.