LG 06/05/2006

September HFT Test at BNL Hardware and Software Requirements

In order to test the functionality of the MIMOSTAR2 read out through a motherboard and check the charged particle environment we will need the following hardware, software and firmware.

Configuration: 3 separate MIMOSTAR2 chips on individual mounts in a telescope configuration as described in HW e-mail. Controlled and read out into a motherboard mounted to a Stratix development board. Trigger and clock come from the MWPC cables as does power. A block diagram is shown below.

Hardware required:

Sensors

- 3 MIMOSTAR2 APS Sensors.

- 3 MIMOSTAR2 readout cables

- 1 set of hardware to hold MIMOSTAR2 sensors in collinear unit.

- 1 set of fixturing pieces to glue sensors to cables

- 1 set of insertion hardware.

- 1 set of mounting brackets / box for motherboard/daughtercard/DDL combo.

- 3 sets of cables (1 end with connectors) to connect the above signals from the MIMOSTAR2 sensors to the motherboard.

Motherboard

- LV PECL receiver for TCD

- Latch up protected power for MIMOSTAR2 sensors

- Cable board connectors for all MIMOSTAR2 sensors

- Santa Cruz interface to Stratix board

- Configurable JTAG (chain of 3 or individual) for MIMOSTAR2 sensors

- JTAG connection for flash and Virtex FPGA on daughtercard.

- Drivers between FPGA and I/O of board.

- Fused Power input

- Cables (individual and chained) for JTAG to PC (Win)

- Cables to monitor and reset latch up

- Power cable to MWPC supply

- Cable to TCD

Stratix Board

- Fused Power input.

- Power Supply / cable

- SODIMM

- SIU + fiber optic cables

- JTAG cable to PC (Win)

- Serial cable to PC (Win)

- Ethernet cable to Platform / PC

PC (Win)

- Fast PC with a lot of RAM

- Provision for multiple JTAG connections

- NI USB DAQ module for Latch up monitor and reset

- Power and Ethernet connection and space on the platform

- Remote reset.

Control PC (Win)

- PC (Win) for control of PC on platform via Timbuktu or some other protocol

- Power and Ethernet connection to the network on the platform.

PC (LINUX)

- PC(LINUX) with lots of RAM

- PCI64 slot for RORC

- RORC

- Power and Ethernet connection.

Firmware Required:

In addition to the framework already laid out, we would like to have the following;

- Interface to the SODIMM on the Stratix Board – if we are going to be saving events and shipping them out of the serial port or over Ethernet, it would be a good thing to use this as a buffer.

- JTAG programming as a bitstream and clock from a FPGA for programming the MIMOSTAR2 chips.

- Ethernet based file transfer via NIOS based Linux.

- TCD and clock handling in the event of not using the ALICE DDL.

Software Required:

- JTAG for chained MIMOSTAR2 chips.

- Some way to send out multiple JTAG from 1 PC to Altera, Xilinx, MIMOSTAR2.

- NI VI to monitor and reset latch up conditions on motherboard.

- Receiver code for serial port.

- Receiver code for TCP/IP (NFS disk mount?)

- Event display.

- Rudimentary online analysis