LG

07/01/2007

Proposal for Ultimate sensor Development Path

I base this development path on the Mimosa8 and Mimosa16 sensors. I suggest two deliverable sensors in the same line.

Stage 1 prototype – Based on Mimosa8/16. Hopefully delivered within 1 year.

- 640 x 640 pixels at 30 µm

- In pixel CDS

- Settable threshold

- Binary readout

- Column parallel shifting at 1 MHz

- 160 MHz RDO clock

- 4 binary outputs / sections – reads out all pixels

- 640 µs integration time

Final Deliverable – Based on Stage 1 prototype with additions

- 640 x 640 pixels at 30 µm

- In pixel CDS

- Settable threshold

- Binary readout

- Column parallel shifting

- <250 MHz RDO clock

- 4 binary outputs / sections – reads out addresses

- 200 µs integration time

- On chip data sparsification

- Triggerable

Some comments:

- This becomes the primary development path and takes priority from previous paths.

- Stage 1 is intended to be a direct descendant of the Mimosa8/16 series with minimal modification.

- Stage 1 is intended for use as both an engineering model and as part of an installed detector patch.

- Keeping the number of columns minimized (30 micron pixels) helps with power dissipation.