M.S. (02/05/2012)

Probe card testing plan

1) power on tests (all LEDs enabled)

- POT  I2C configuration

(if problems with this mode, we can use VDDA for powering Analog and Digital parts of the chip)

- ADC  I2C readout for power supply monitoring and VREF scans

(try to implement a power-on sequence) (02/08/2012)

2) functionality tests

- analog PWR enable

- led flash circuit

- seal source motor control

3) ultimate sensor tests

- test chip ID

- test chip JTAG configuration

- test chip power consumption (I2C ADC)

- default VREF2 settings:		we need to check if this parameter varies between different sensors and find a way for automatic characterization of VREF2 (procedure?)

- test VREF2 (VREF1 ?) linearity

- (IO delay?)

- threshold scan (test mode) 	- extract offset, threshold=0, noise level for 1e-4, 1e-5 ?

- test for faulty pixels (test mode, 928 LED flashes) Threshold=5 x noise (or more ?)

- test pattern mode, full rdo - verify data reconstruction (test different headers, trailers,encoded patterns)

- full RDO test with known noise levels e.g. 1e-4 - check for match with threshold scan

- test temperature diode (procedure?) - not needed for probetesting, will be done in ladder tests (02/08/2012)

- configure chip for analog readout

- analog data acquisition (superframes)

PXL sensor full testing sequence:

- chip ID

- PWR

- JTAG config (2-3 tests seqences)

- PWR

- start (which settings?)

- PWR

- VREF2

- threshold scan

- LED test

- normal RDO tests

- analog tests

LOGGING RESULTS INTO OUR DATABASE

discussion 2-14-2012

date+time, wafer, location, test type (probe test, ladder test), operator name, data path info, comments

(temperature)

- power on					=> 	I/V

- chip ID 					=>	jtag error level

- test JTAG response	(a few sequences)	=> 	error codes

- PWR meas  for default settings		=> 	I/V

- DAC scan for VREF2			=>	VREF2

- threshold scan				=> 	threshold and noise  x4

- PWR meas for scan mode			=> 	I/V

- LED test					=>	hot/dead pixels

- PWR meas for LED test			=> 	I/V

- analog test 					=> 	noise, sigma, peak, sigma

- PWR meas for analog test			=> 	I/V

x3 for different voltages