Excerpt from MEMOSA5OpertionLog.doc

on:   mim5_als5g.mcs

All the sudden data is transferring again and the timing is right for a triggered run at the ALS,  only problem is that it skips every other event.

Updated the table see below and found some pin out errors carried from previous copies

Snap shot:  mim5_als5g

trg_scope   yellow

wr_en green

frame_marker  purple

stretcher width set to match one frame write

| Generic parameter | MODULE | mim5_als5g.mcs |
| --- | --- | --- |
| RST_DLY | acq_mimosa | 1 |
| ADC_DLY |  | 10 |
| ROW_CNT |  | 512 |
| COL_CNT |  | 512 |
| NUM_TRGT |  | 2*512*512 |
| ACQ_CNT |  | 4*512*512 |
| DLY_SYNC | trigger | 1491924 |
| SKIP_EVNTS |  | 2 |
| ACQ_CNT | mac_if5 | 4*512*512 |
| WDTH_CNT | leddriver | 1 |
| WAIT_CNT |  | 2 |
| WIDTH | frame_marker | 262144 |

| FPGA File: | mim5_als5g.mcs |  |
| --- | --- | --- |
| J11 test point numbering J11-25 = 1 J11-23 = 2 …. | input and output names on print | FPGA pins | Connection |
| 1 | J11_25 | R18 | pulser_out |
| 2 | J11_23 | R19 | trgt_frame_all |
| 3 | J11_21 | R20 | wr_en |
| 4 | J11_19 | R21 | rd_en |
| 5 | J11_17 | R22 | req_in1 (ack from NI board) |
| 6 | J11_15 | P19 | sync_trg_scope |
| 7 | J11_13 | P20 |  |
| 8 | J11_11 | P21 | grd to auto trigger |
| 9 | J11_9 | P22 | section(0) (pulled up) |
| 10 | J11_7 | P18 | section(1) (pulled up) |
|  | J11_5 | N18 | acq_en if floating |
| 12 | J11_3 | N19 | mk_sync (open to select) |
| 13 | J11_1 (reset) | N20 | reset (pulled up) |
| J12 | J12_25 | AA20 |  |
|  | J12_23 | W20 |  |
| J8 ALS connections |  |  |  |
|  | J8_3 | V5 | FRAME MARKER (MarTest) frame_marker (6.5 ms) (APS4)(red?) |
|  | J8_1 | U5 | ALS LATCHED (MarTest) trg_scope (50 ms) (APS4)(brn?) |
| J10 ALS | J10_1 | AB13 | ALS TRIGGER input (grn ribbon) |

mim5_als5g.mcs

tested on

mother board 7

mimosa5 mezz 17

gave the following results (may have not been with CDS, but looked the same with CDS on) on LabView: