Full :    1   clusterfifo is full,  0 clusterfifo is OK

Align:   0  data is not aligned with chip marker, 1 data alignment is OK

Sram :   1  sram controller is in error state, 0  sram controller is OK

Adc  :    0   ADC’s DCM is not locked, 1 ADC’s DCM is locked

The above is normal data format, which is also true for later HFT test and maybe few modification until final data format. For ALS test ,one event has 3 blocks corresponding 3 chips. The ender of whole event is 0x55555555.  The Data length is the number of clusters in the block, excluding the header and ender.

The fullframe data format is

Trigger flag  being 1 means the frame data comes with trigger.

One frame has 84480 items including 2 real frames and 8 dummy frames. The ALS data only records real frame. Thus one frame has 8448*2 items. Since the high 16 bit always 0, the fullframe data in ALS test is save as “short int” type by “fwrite(data,1,2,file);”

One can use fread(data,1,2,file) to get  a item of fullframe data. And use fread(data,8448*2,2,file) to get one whole frame.

# Text boxes

14b

0

block…

blocklast

header

Address

Address

Address

Address

Address

Address

……

ender

AAAAAAAA

32b(bits)

0

12b

4b

trig

4b

daq

12b

token

0

12b

Chip ID

20b

0

20b

Data length

12b

0

14b

R threshold

9b

C threshold

9b

adc

sram

align

0

full

0

1b

1b

1b

9

1b

23b

32b

0

0

1

2

3

4

5

6-15

32b(bits)

EEEEEEEE

block2

block1

18b

address

Event

For

Trig

Two

Event

For

Trig

one

Event

For

Trig

……

12b

ADC value

1b

Trigger flag

19b

0

Frame1

Frame2

Frame3