Chip correlation program

In ALS test, we use a telescope composed by three MIMOSTAR chips. These chips are parallel and perpendicular to the beam. The displacement between two chips can be mainly characterized by three parameters x , y , , which represent the displacement in x, y direction and the rotation angle in z direction.

To get x and y, we plot histogram of the difference of x and y coordinates of two clusters from two chips. For example, cluster A comes from chip0, cluster B comes from chip1. One does the subtraction of two x coordinates of A and B, getting the difference x, repeat this procedure for every cluster in chip0 and chip1. The histogram of x is the result we want for measuring x.

The first row of below picture shows the histogram for x.

The second row of below picture shows the histogram for y.

From left to right, chip pair are 01 02 12

We can see the peak clearly. And the discontinuity of the first row is caused by the masked mark pixels.

to get the rotation parameter, we should draw two dimension histogram of x with y or y with x. the picture below shows the result.

The first row of below picture shows the histogram for x and y.

The second row of below picture shows the histogram for y and x.

From left to right, chip pair are 01 02 12

The fit of these pictures roughly tell us the value of x , y , and .