## Slide 1
LBNL
Leo Greiner, Eric Anderssen,
Thorsten Stezelberger, Joe Silber, Xiangming Sun, Michal Szelezniak, Chinh Vu,
Howard Wieman
UTA
Jerry Hoffman, Jo Schambach
IPHC Strasburg
Marc Winter CMOS group
STAR Pixel Detector
Probe Testing

## Slide 2: Talk Outline
Phase-1/2 probe testing system design
Current capabilities
Ultimate sensor probe testing
Summary

## Slide 3: Probe Test System Design
Probe
Card
Probe
Station
Power
Supply
RDO Board
Control
PC
CUSTOM
USB
SERIAL
POWER
The probe test system
is based on our prototype
readout board.

## Slide 4: Probe Testing Mechanical Design
Vacuum chuck for probe testing 20 (50 μm thick) MAPS sensors per testing session.
Automated test system based on the prototype RDO system gives a qualitative analysis of probed sensors including identification of dead/stuck pixels/columns.

## Slide 5: Phase-1 Probe Card
Ribbon cable connection to RDO Board
Analog buffering
Probe pins
Digital section
55Fe source shield
Power regulation/switching

## Slide 6: Probe card testing
We wire bond a sensor to the probe card to test the full functionality of the probe card and testing system before the probes are mounted to the card.

## Slide 7: System Attributes
We have a scripted probe testing setup based on our individual testing board scripts.
We test at full RDO speed of 160 MHz.
Power is regulated and switched on the probe card.
Transfer function data is taken and analyzed in root with scripts.

## Slide 8: Sensor Test Sequence
Current draw (power on)
Chip id (JTAG)
Test JTAG multiple patterns
Load Default JTAG
Measure current draw
Measure DACs - scan VREF2, then scan to find VREF1 so that threshold = 0
threshold scan
LED test + power consumption
Analog RDO noise measurement on all sensors
Source measurement on 1 sensor/wafer
Repeat sequence for 3.0V and 2.9V
All results are saved to a database that will be used for selecting sensors to build into ladders and sectors and for building configuration JTAG commands.

## Slide 9: Ultimate Sensor Probe Card
Based on the successful Phase-1 probe card.
Schematic in progress at LBNL
Expected to be complete by September 15
Is IPHC interested in probe cards for Ultimate?

## Slide 11: PXL Mechanical Construction
PXL Mechanical
D-tube and sectors
Ladder fixturing
Vacuum chuck for 50um sensors