## Slide 1: STAR-PXL Mechanical Integration and Cooling
St. Odile Ultra-Thin Vertex Detector Workshop
8-Sept-2011
Howard Wieman
LBNL

## Slide 2: PIXEL Mechanical Work
Leo Greiner
Eric Anderssen
Hans Georg Ritter
Michal Szelezniak
Xiangming Sun
Joseph Silber
Jim Thomas
Howard Matis
Mario Cepeda
Tom Johnson
Dan DeBoer
Brian Bentley
University of Texas Austin:
Jerry Hoffman
Herbert Boehl
Jo Schambach
Lawrence Berkeley National Lab:

## Slide 3: Pixel geometry
2.5 cm radius
8 cm radius
Inner layer
Outer layer
End view
One of two half cylinders
20 cm
 coverage +-1
total 40 ladders

## Slide 4: Topics
Mechanical trade offs in achieving the highest pointing precision
Work addressing mechanical precision and stability.
Rapid Detector Replacement

## Slide 5: vertex projection from two points
detector layer 1
detector layer 2
pointing resolution = (13  22GeV/pc) m
from
detector
position
error
from
coulomb
scattering
r2
r1
true vertex
perceived
vertex
x
x
v
r2
r1
true vertex
perceived
vertex
v
m
expectations for the HFT pixels
first pixel layer
more than 3 times
better than hybrids

## Slide 6: Know where the pixels are
Build a mechanically stable structure
Measure pixel locations – i.e. generate a spatial pixel map that will not be corrupted by mechanical changes

## Slide 7: development of spatial map
Bob Connors
Spiros Margetis
Yifei Zhang
touch probe 2-3 m (xyz) and
visual 2-3 m (xy) 50 m (z)
active volume: huge
10 gm touch
probe force
visual sub micron (xyz) repeatability
5 m accuracy over active volume
Feather light touch probe
active volume:
30 in X 30 in X 12 in
MEMOSTAR3, 30 m pitch

## Slide 8: Mechanical Stability
Movement induced temperature changes
Deflection from gravity
Vibration movement from mounts in STAR
Movement induced by cooling air
  vibration and static displacement
Once the pixel positions are measured will they stay in the same place to within 20 µm? Issues addressed:

## Slide 9: Stability requirement drove design choices
The detector ladders are thinned silicon, on a flex kapton/aluminum cable
The large CTE difference between silicon and kapton is a potential source of thermal induced deformation even with modest 10-15 deg C temperature swings
Two methods of control
  ALICE style carbon composite sector support beam with large moment of inertia
  Soft decoupling adhesive bonding ladder layers
Multiple designs were considered. This design optimized low X0, mechanical stability and ease of fabrication

## Slide 10: Ladder design with soft adhesive (6 psi shear modulus)
cable bundle
drivers
pixel chips
adhesive
wire bonds
capacitors
adhesive
composite backer
kapton flex cable
adhesive:
3M 200MP
2 mil, film adhesive

## Slide 11: FEA analysis showing bi-metal thermally induced deformation
ladder cross section
short direction
rigid bond
500 micron deformation
20 deg C temperature change
soft adhesive
4.3 micron deformation

## Slide 12: FEA analysis of thermally induced deformation of sector beam
FEA shell elements
Shear force load from ladders
20 deg temperature rise
Soft adhesive coupling
200 micron carbon composite beam
end cap reinforcement
Maximum deformation 9 microns (30 microns if no end cap)

## Slide 13
Center Ladder Deflection With Temperature
Preliminary
1.3 m/deg C measured
0.5 m/deg C FEA
Larger than predicted, but acceptable

## Slide 14: FEA analysis - sector beam deformation – gravity load
FEA shell analysis
120 micron wall thickness composite beam
gravity load includes ladders
maximum structure deformation 4 microns
ladder deformation only 0.6 microns

## Slide 15
Air cooling of PXL detector
CFD analysis
Cooling tests with full size mockup

## Slide 16: Air cooling of silicon detectors - CFD analysis
air flow path – flows along both inside and outside surface of the sector
Silicon power: 100 mW/cm2 (~ power of sunlight)
240 W total Si + drivers

## Slide 17: Air cooling – CFD analysis
air flow velocity 9-10 m/s
maximum temperature rise above ambient: 12 deg C
sector beam surface – important component to cooling
dynamic pressure force 1.7 times gravity
stream lines with velocity
silicon surface temperature
velocity contours

## Slide 18: Detector mockup
Driver section ~6 cm
Sensor section ~20 cm
5 | 1 | 6
3 | 2 | 4
Kapton cables with copper traces forming heaters allow us to dissipate the expected amount of power in the detector
There are 6 thermistors on each ladder (except for the ladder with silicon chips mounted) that allow us to monitor their temperature with an automated measurement system based on the Touch-1 cable tester
One of the sectors (sector 1) was equipped with 10 dummy silicon chips per ladder, with Pt heaters deposited on top of silicon

## Slide 19: Setup

## Slide 20: Setup

## Slide 21: Cooling tests at ~360 W – IR images
Air 13.8 m/s Hot spots ~10 °C above input
Air 10.1 m/s Hot spots ~14 °C above input
Air 4.7 m/s Hot spots ~21 °C above input
Input air temperature ~27 °C

## Slide 22: Cooling Tests at ~340 W
Observations:
Mid-section is the hottest part of the ladder
max temperature increase above ambient is
  ~ 8 °C @ 13.8 m/s
  ~12 °C @ 10.1 m/s
  ~17 °C @ 4.7 m/s
unsuported end
mid-section
fixed end
Solid – inner layer
Open – outer layer

## Slide 23
Analysis and testing of vibration induced by cooling air

## Slide 24: vibration modes with reinforced end cap
The message
  Lots of complicated modes close in frequency
  End cap raises frequencies a bit
259 Hz
397 Hz
276 Hz
441 Hz
497 Hz

## Slide 25: wind tunnel setup to test vibration and displacement
air velocity probe
two positions
shown
capacitance vibration probe
two positions shown
carbon fiber sector beam
adjustable
wall for air
turn around
air in
air out
C:\Documents and Settings\Howard Wieman\My Documents\aps project\mechanical\PXL phase 1 sept 2008\sector ph1 wind tunnel.SLDASM

## Slide 26: wind tunnel

## Slide 27: capacitive probe vibration measurements
air velocity 2.7 m/s
position signal, 25 m/volt
air velocity 9.5 m/s
position signal, 25 m/volt
log FFT, peak at 135 Hz

## Slide 28: Ladder vibration induced by cooling air
system resolution limit
all errors
desired vibration target
required air velocity
18 mph
no reinforcement at the end

## Slide 29: measured static deformation from 9 m/s air flow
-167 µm
6 µm
17 µm
17 µm
-179 µm
-248 µm
-156 µm
-163 µm
-113 µm
9 µm
11 µm
1 µm
open end
reinforced
end

## Slide 30: measured vibration (RMS) induced by 9 m/s air flow
13 µm
14 µm
14 µm
4 µm
6 µm
6 µm
8 µm
3 µm
3 µm
2 µm
11 µm
4 µm
open
end
reinforced
end

## Slide 31
PXL insertion mechanism for rapid detector replacement

## Slide 32
PXL detector centered in STAR
in the Middle Support Cylinder (MSC)
single end support allows rapid insertion and removal
Can replace PXL detector with less than day of shut down

## Slide 33
Insertion and closing about the beam pipe
open to clear beampipe flanges
closing down
fully inserted and locked in kinematic mounts

## Slide 34
insertion mechanism
carriage rides on support rails
kinematic mounts engage at center position
cam and guides control lateral location during insertion
hinge mechanism for lateral motion
mechanical release to transfer load to kinematic mounts
thin carbon half tube for PXL support and cooling air duct

## Slide 35
Mechanical systems are being fabricated and tested
Stability is satisfactory
End of Presentation

## Slide 36
Backup
extra

## Slide 37: Development of sector beam and ladder fabrication
Eric Anderssen and Tom Johnson have been working on fabrication methods for:
  Sector Beam
  and Ladders
Produced sample beams, 244 m thick, 7 ply, 21 gm
expected ladder mass 7.5 gm
ladders
sector beam

## Slide 38: ladder to sector out2 bond fixture in the shops
ladder to out2 bond fixture.SLDASM
(designed to allow ladder replacement)

## Slide 39: sector chuck parts
locating pin MMC 8472A11.SLDPRT
bullet nose liner MMC 31335A51, 1 of 3
bullet nose aligning pin MMC 31335A11, 1 of 2
bullet nose diamond aligning pin MMC 31335A31
1.5 in post hex MMC 91780A361, 1 of 4
sector chuck out2 base.SLDPRT
sector chuck out2 cap.SLDPRT
plunger pin 1lb MMC 3360A560, 1 of 2
locating pin diamond MMC 8472A19.SLDPRT
¼-20 x 1.5 in, 1 of 4
¼-20 x 1 in, 1 of 2
z locator.SLDPRT

## Slide 40: ladder chuck parts
ladder chuck handle.SLDPRT, 1 of 2
plunger pin 3 lb MMC 3360A330, 1 of 4
ladder chuck.SLDPRT
¼-20 x 1in, 1 of 4
ladder chuck.SLDASM

## Slide 41: out2 silk screen assembly for applying glue that holds ladder to the sector
stainless surface 25 mil
above aluminum surface
out2 silkscreen frame.SLDPRT
sized for 2 mil bond line between
stainless and aluminum
this surface is initially shimmed by 20 mils to be 5 mils below the stainless surface. This is to permit future adjustment

## Slide 42: ladder assembly fixture
3/8 OD tube connection to
vacuum
¾ ID tube connection to
1 gallon vacuum ballast tank
vacuum release valve for
hold down of the vacuum chucks
vacuum distribution manifold
vacuum chuck system for placing chips and other ladder parts

## Slide 43: ladder fixture
ladder fixture.SLDASM
vacuum chuck system for placing chips and other ladder parts

## Slide 44: Sector structures

## Slide 45: ladder fabrication and tooling

## Slide 46: ladder fabrication and tooling

## Slide 47: ladder fabrication and tooling
finalizing mechanical designs and developing rapid production methods

## Slide 48: ladder fabrication and tooling
ladder with
silicon heater
chips
(50 m thick)

## Slide 49: Testing equipment used in cooling measurements
The tests we wanted to perform required measuring
  Air flow
  Input and output air temperature
  Ladder temperature
  Ladder vibrations
Equipment used:
  Industrial 1.1 KW air pump (dust collector) RD-211 → provided air flow
  Air velocity transducer FMA-905-I from Omega → air flow measurements
  K-type thermocouples → air temp. meas.
  Negative temperature coefficient (NTC) thermistors → ladder temp. monitoring
  Touch-1 cable tester from Cirris → automated temp. meas.
  Python-based visualization software → automated temp. monitoring
  Infrared camera → ladder temp. monitoring
  C1-A capacitive probe from the Lion Precision Co. → ladder vibration meas.

## Slide 50: vibration modes – preliminary – better composite numbers available
229 Hz
316 Hz
224 Hz
473 Hz
348 Hz

## Slide 51: Vibration from STAR support, accelerometer measurement
detector vibration from STAR support < 0.1 micron RMS

## Slide 52: Vibrations caused by airflow
Sector 1, Ladder 2
Beginning of the driver section
(Supported end)
End of sensor section
(Unsupported end)
coupled means that the unsupported end is tied to sector 2
(coupled )
(coupled )
(coupled )

## Slide 53: wind tunnel, rapid prototype parts from model
air flow control
parts built with
3D printer
parts built with SLA, stereolithography apparatus