## Slide 1: Getting Started with EPICS Lecture Series
State Notation Language and the Sequencer
John Maclean
11/09/04

## Slide 2: Outline
What is State Notation Language (SNL)
Where does it fit in the EPICS toolkit
Components of a state notation program
Some Notes on the Runtime Sequencer
Building, running and debugging a state notation program
Additional Features
When to use it
This talk covers Sequencer version 2.0.8
This talk does not cover all the features of SNL and the sequencer. Consult the manual for more information.
  http://www.slac.stanford.edu/comp/unix/package/epics/sequencer/

## Slide 3: SNL and the Sequencer
The sequencer runs programs written in State Notation Language (SNL)
SNL is a ‘C’ like language to facilitate programming of sequential operations
Fast execution - compiled code
Programming interface to extend EPICS in the real-time environment
Common uses
  Provide automated start-up sequences like vacuum or RF where subsystems need coordination
  Provide fault recovery or transition to a safe state
  Provide automatic calibration of equipment

## Slide 4: Where’s the Sequencer?
Channel Access
LAN
Device Support
I/O Hardware
IOC
The major software components of an IOC (IOC Core)
Database
Sequencer

## Slide 5: Where’s the Sequencer Now?
MEDM
Client
Client
Client
MEDM
Server
IOC
IOC
Meter
Power Supply
Camera
IOC
Tools
Sequencer
LAN

## Slide 6: The Best Place for the Sequencer
From Sequencer Version 2.0.0 can be either in the IOC or on a workstation
Traditionally in the IOC
Locating it in the IOC probably makes it easier to manage
Running on workstation could make testing easier
Workstation gives an easy way to write the CA parts of CA clients

## Slide 7: SNL implements State Transition Diagrams
State A
State B
Event
Action
Transition
A to B

## Slide 8: STD Example
Start
Low vacuum
High vacuum
pressure > 5.1 uTorr
Open the valve
pressure < 4.9 uTorr
Close the valve

## Slide 9: Some Definitions
SNL : State Notation Language
SNC : State Notation Compiler
sequencer : The tool that executes the compiled SNL code
Program : A complete SNL application consisting of declarations and one or more state sets
State Set : A set of states that make a complete finite state machine
State : A particular mode of the state set in which it remains until one of its transition conditions is evaluated to be TRUE

## Slide 10: SNL: General Structure and Syntax
program program_name
declarations
ss state_set_name {
  state state_name{
  entry{
  action statements
  }
  when (event){
  action_statements
  } state new_state_name
  when(event)
  ...
  exit{
  action statements
  }
  }
  state state_name{
  ...
  }
}

## Slide 11: SNL: General Structure and Syntax
Program name A Program contains many state sets. The program name
        is used as the handle to the sequencer manager for state programs.
ss name { A state set becomes a task in the vxWorks environment.
state name{ A state is an area where the task waits for events.
The related task waits until one of the events occurs and
then checks to see which it should execute. The first state
defined in a state set is the initial state.
option flag; A state specific option
when(event) { Is used to define the events for which this state waits.
}state statename Is used to define the new state after the actions are taken.
entry{ Do these actions on entry to this state from another state (using option -e; will do these actions even if it enters from the same state)
}
exit{ Do these actions before exiting this state to another state.
(using option -x; will do these actions even if it exits to the same state.)
}

## Slide 12: Declarations
Occur before a state set and have a scope of the entire program.
Scalar types
  int variableIname;
  short variableSname;
  long variableLname;
  char variableCname;
  float variableFname;
  double variableDname;
  string variableStrname; /* currently limited to 40 characters*/
Vector types
  int arrayIname[array_length];
  short arraySname[array_length];
  long arrayLname[array_length];
  char arrayCname[array_length];
  float arrayFname[array_length];
  double arrayDname[array_length];

## Slide 13: Declarations - Assignments
Assignment to channel access server channels
  float pressure;
  assign pressure to “CouplerPressureRB1”;
  double pressures[2];
  assign pressures to {“CouplerPressureRB1”, ”CouplerPressureRB2”, ” CouplerPressureRB3”};
To use these channel in when clauses, they must be monitored
  monitor pressure;
  monitor pressures;
Can be written like this to aid readability
float pressure; assign pressure to “PressureRB1”; monitor pressure;

## Slide 14: Declarations – Event Flags
Declaring Event Flags
  Event for state sets to set, clear and test
  evflag event_flag_name;
  Flag monitor is set when PV changes (posts a monitor)
  evflag flag_monitor;
  sync pressure flag_monitor;

## Slide 15: Events
An event is the condition on which statements following a when are executed and a state transition is made
Possible events:
Change in value of a variable that is being monitored
example: when(achan < 10.0)
A timed event (not a task delay!)
  example: when(delay(1.5))
  The delay value is in seconds. It is delclared internally as a double and constant arguments to the delay function must contain a decimal point.
  A delay is normally reset whenever the state containing it is exited. Use the state specific option -t to keep it from being reset when exiting to the same state..

## Slide 16: Events (continued)
An internally generated event (event flag)
  examples: when(efTestAndClear(myflag))
  when(efTest(myflag))
  efTest does not clear the flag. efClear must be called sometime later to avoid an infinite loop.
  The event flag can be set internally by efSet(event_flag_name)
  or if the flag is synced to a monitored channel it will be set when
  the channel changes.
Change in the channel access connection status.
  examples: when(pvConnectCount() < pvChannelCount())
  when(pvConnected(mychan) )

## Slide 17: Actions
Built-in action function, e.g. :
  pvPut (variable_name);
  pvGet (variable_name);
  efSet (event_flag_name);
  efClear (event_flag_name);
Almost any C expression
  switch is not implemented and code using it must be escaped.
  %% escape one line of C code
  %{
  escape any number of lines of C code
  }%

## Slide 18: Example - State Definitions and Transitions
pressure > .0000051
RoughPump on
CryoPump off
Valve closed
pressure <= .0000049
RoughPump off
CryoPump on
Valve open
pressure <= .0000049
RoughPump off
CryoPump on
Valve open
pressure > .0000051
RoughPump on
CryoPump off
Valve closed
10 minutes
RoughPump off
CryoPump off
Valve closed
Initial State
Fault
High Vacuum
Low Vacuum

## Slide 19: Example - Declarations
double pressure;
assign pressure to “Tank1Coupler1PressureRB”;
monitor pressure;
short RoughPump;
assign RoughPump to “Tank1Coupler1RoughPump”;
short CryoPump;
assign CryoPump to “Tank1Coupler1CryoPump”;
short Valve;
assign Valve to “Tank1Coupler1IsolationValve”;
String CurrentState;
assign CurrentState to “Tank1Coupler1VacuumState”;

## Slide 20: Example – State Transitions
program vacuum_control
ss coupler_control
{
state init{
when(pressure > .0000051){
} state low_vacuum
when(pressure <= .0000049){
} state high_vacuum
}
state high_vacuum{
when(pressure > .0000051){
} state low_vacuum
}
state low_vacuum{
when(pressure <= .0000049){
}state high_vacuum
when(delay(600.0)){
}state fault
}
state fault{
}
}

## Slide 21: Example – Init State
state init {
entry {
strcpy(CurrentState,”Init”);
pvPut(CurrentState);
}
when(pressure > .0000051){
RoughPump = 1;
pvPut(RoughPump);
CryoPump = 0;
pvPut(CryoPump);
Valve = 0;
pvPut(Valve);
} state low_vacuum
when(pressure <= .0000049){
RoughPump = 0;
pvPut(RoughPump);
CryoPump = 1;
pvPut(CryoPump);
Valve = 1;
pvPut(Valve);
} state high_vacuum
}

## Slide 22: Example – State low_vacuum
state low_vacuum{
entry{
strcpy(CurrentState,”Low Vacuum”);
pvPut(CurrentState);
}
when(pressure <= .0000049){
RoughPump = 0;
pvPut(RoughPump);
CryoPump = 1;
pvPut(CryoPump);
Valve = 1;
pvPut(Valve);
}state high_vacuum
when(delay(600.0)){
}state fault
}

## Slide 23: Example – State high_vacuum
state high_vacuum{
entry{
strcpy(CurrentState,”High Vacuum”);
pvPut(CurrentState);
}
when(pressure > .0000051){
RoughPump = 1;
pvPut(RoughPump);
CryoPump = 0;
pvPut(CryoPump);
Valve = 0;
pvPut(Valve);
} state low_vacuum
}

## Slide 24: Example – State fault
state fault{
entry{
strcpy(CurrentState,”Vacuum Fault”);
pvPut(CurrentState);
}
}

## Slide 25: Building an SNL program
Use editor to build the source file: file name must end with ".st", e.g. "example.st".
“make” automates these steps:
  Optionally runs the C preprocessor
  Compiles the state program with SNC to produce C code:
    snc example.st -> example.c
  Compiles the resultant C code with the C compiler:
  cc example.c -> example.o
  The file "example.o” becomes part of the application library, which is ready to be loaded by VxWorks.
  For Unix systems an executable file “example” is created

## Slide 26: Run Time Sequencer
The sequencer executes the state program.
The sequencer supports the event-driven execution; no polling needed.
Each state set becomes a VxWorks task or UNIX thread.
The sequencer manages connections to database channels through "channel access".
The sequencer provides support for channel access (put, get, and monitor).
The sequencer supports asynchronous execution of delay, event flag, pv put and pv get functions.
Only one copy (object module) of the sequencer is required on an IOC.
Query commands display information about executing state programs.

## Slide 27: Executing a State Program – IOC
Assumes you are at an IOC console and database is loaded
Load the sequencer
  ld < pvLibrary
  ld < sequencer
Load a state program
  ld < example.o
Execute program
  seq &vacuum_control
Er… That’s it! Exercise program
To stop program
  seqStop vacuum_control

## Slide 28: Debugging
Use special state program query commands:
  seqShow
    displays information on all running state programs
  seqShow vacuum_control
    displays detailed information on program
  seqChanShow vacuum_control
  displays information on all channels
  seqChanShow vacuum_control,-
    displays information on all disconnected channels

## Slide 29: Debugging (continued)
Use printf functions to print to the console
  printf("Here I am in state xyz \n");
Put strings to pvs
  sprintf(seqMsg1, "Here I am in state xyz");
  pvPut(seqMsg1);
Reload and restart
  seqStop vacuum_control
  Edit
  ld < example.o
  seqStart &vacuum_control

## Slide 30: Debugging - seqShow
seqShow
epics> seqShow Program Name Thread ID Thread Name SS Name stabilizer ede78 stabilizer stabilizerSS1 beamTrajectory db360 beamTrajectory bpmTrajectorySS autoControl ed620 autoControl autoCtlSS

## Slide 31: Debugging - seqShow
seqShow stabilizer
epics> seqShow stabilizer State Program: "stabilizer" initial thread id = ede78 thread priority = 50 number of state sets = 1 number of syncQ queues = 0 number of channels = 3 number of channels assigned = 3 number of channels connected = 3 options: async=0, debug=0, newef=1, reent=0, conn=1, main=0 State Set: "stabilizerSS1" thread name = stabilizer; thread id = 974456 = 0xede78 First state = "init" Current state = "waitForEnable" Previous state = "init" Elapsed time since state was entered = 88.8 seconds

## Slide 32: Debugging - seqChanShow
seqChanShow stabilizer
epics> seqChanShow stabilizer State Program: "stabilizer" Number of channels=3 #1 of 3: Channel name: "jfm:OP:stabilizerC" Unexpanded (assigned) name: "{user}:OP:stabilizerC" Variable name: "enableButton" address = 154120 = 0x25a08 type = short count = 1 Value = 0 Monitor flag = 1 Monitored Assigned Connected Get not completed or no get issued Put not completed or no put issued Status = 17 Severity = 3 Message = Time stamp = <undefined> Next? ( skip count)

## Slide 33: Additional Features
Connection management:
  when ( pvConnectCount() != pvChannelCount() )
  when ( pvConnected(Vin) )
Macros:
  assign Vout to "{unit}:OutputV";
  (must use the +r compiler options for this if more than one copy of the sequence is running on the same ioc)
  seq &example, "unit=HV01"
Compiler options:
  +r make program reentrant (default is -r)
  -c don't wait for all channel connections (default is +c)
  +a asynchronous pvGet() (default is -a)
  -w don't print compiler warnings (default is +w)
  +e eftest automatically clears flag (default is -e)

## Slide 34: Additional Features (continued)
Access to alarm status and severity:
  pvStatus(var_name)
  pvSeverity(var_name)
Queueable monitors -- saves monitors in queue in the order they come in -- no missing monitors.
  syncQ variableName to eventFlagname [optionally the length of the queue]
  pvGetQ( variableName )
    removes oldest value from variables monitor queue. Remains true until queue is empty.
  pvFreeQ( variable Name)

## Slide 35: Advantages
Can implement complicated algorithms
Can stop, reload, restart a sequence program without rebooting
Interact with the operator through string records and mbbo records
C code can be embedded as part of the sequence
All Channel Access details are taken care of for you
File access can be implemented as part of the sequence

## Slide 36: When to use the sequencer
For sequencing complex events
E.g. Parking and unparking a telescope mirror
Photograph courtesy of the Gemini Telescopes project

## Slide 37: Should I Use the Sequencer?
START
CAN I DO THIS IN A DB?
Y
N
CAN I DO THIS IN A DB?
Y
N
USE THE SEQUENCER
USE A DATABASE
END

## Slide 38: Acknowledgements
Slides for this presentation have been taken from talks prepared by the following people
  Bob Dalesio (LANL/SNS/LCLS)
  Deb Kerstiens (LANL)
  Rozelle Wright (LANL)
  Ned Arnold (APS-Controls)