## Slide 1: Getting Started With EPICS Lecture Series Writing Record Support
Marty Kraimer, ASD/Controls
23 November 2004

## Slide 2: Overview
Record Support
  Implements a Record Type
  Plugs into database common environment
Implementation steps
  Prepare a Database Definition (.dbd) file
  Create a C source file which implements semantics
  Start with existing support!!!
Documentation
  App Dev Guide 3.14.6 - Chapters 5, 6, and 11
  makeBaseApp example - xxxRecord
  base/src/rec
BUT FIRST: Ask the question Why?
  Reasons against a new record type
  Reasons for a new record type

## Slide 3: Reasons Against a New Record Type
Only one STAT, SEVR, VAL
  Example: Power Supply Record, i.e. multiple inputs, outputs. What do stat and sevr mean?
  Is a template of standard record types a better choice?
No device support
  Standard record types have extensive associated device support
No documentation. You should also provide it.
Can be tricky to implement proper semantics
Some standard tools may also need extensions. Example capFast.

## Slide 4: Reasons For a New Record Type
Sets of standard record types will not satisfy need
  Are you really sure? Think hard!!!
State must be shared across multiple records
  Example asynRecord – Can dynamically change hardware addressing
    I implemented via device support and standard records. Complicated!!
    Mark implemented via new record type. Much easier to understand.
Many record instances: Example mbbiDirect record type.
Because it is fun. NOT A GOOD REASON.
Example Event Generator/ Event Receiver Records
  APS/SLS/Diamond/PLS – Special Record Types
  SNS has different event system.
    Question: Modify EG/ER or write device support for standard records?
    Answer: Not clear!!!
      Very few EG records
      At most one ER per IOC
      I think SNS decided to use device support for standard record types

## Slide 5: Implementation: Create DBD.
Create a Database Definition (dbd) File.
Chapter 6 of 3.14.6 Application Developer’s Guide.
Syntax
  recordtype(<recordtype>) {
  include “dbCommon.dbd”
  field(<fieldname>,<fieldtype>) {
  <fieldattributes>
  }
  field(<fieldname>,<fieldtype>) {
  <fieldattributes>
  }
  ...
  }

## Slide 6: DBD Example
Example
  recordtype(example) {
  include “dbCommon.dbd”
  field(PREC,DBF_DOUBLE) {
  prompt(“Display Precision”)
  promptGroup(GUI_DISPLAY)
  }
  field(VAL,DBF_DOUBLE)
  }

## Slide 7: DBD continued
recordtype(<recordtype>) Should be alphanumeric starting with letter
include “<filename>”
  Must include dbCommon first.
field(<fieldname>,<type>) {<attributes>}
  Fieldname should be alphanumeric starting with letter
  Length is normally limited to four characters
    3.14 allows arbitrary length
    May cause problems with some Channel Access clients
  In dbd file this should be upper case. It is converted to lower case when the <recordtype>.h file is generated. Bad decision!!

## Slide 8: DBD – Field Attributes
<fieldattributes>
  asl : access security level
    ASL1 - Fields seldom modified - default
    ASL0 - Fields meant to be modified
  initial : initial value
  prompt : string for Database Configuration
  promptgroup : Should DCT allow field to be configured?
  special: Special handling on put
    Several values
    SPC_MOD, SPC_DBADDR, SPC SPC_NOMOD

## Slide 9: DBD – Field Attributes continued
<fieldattributes> (continued)
  pp : process passive record on put?
  interest : interest level used by dbpr (Database Print Record)
  base : DECIMAL (default) or HEX (Only used by dbDumpRecord)
  size : For DBF_STRING
  extra : For DBF_NOACCESS
  menu : For DBF_MENU.

## Slide 10: DBD - Fieldtypes
<fieldtype>
  DBF_STRING
  DBF_CHAR DBF_UCHAR
  DBF_SHORT DBF_USHORT
  DBF_LONG DBF_ULONG
  DBF_FLOAT DBF_DOUBLE
  DBF_ENUM
  DBF_MENU
  DBF_DEVICE
  DBF_INLINK DBF_OUTLINK
  DBF_FWDLINK
  DBF_NOACCESS

## Slide 11: DBD String Field
DBF_STRING fields
  Fixed length null terminated strings
  Channel access support max of 40 characters
  Arrays of character strings are possible
Example
  field(VAL,DBF_STRING) {
  size(40)
  prompt(“value”)
  promptgroup(GUI_DISPLAY)
  }

## Slide 12: DBD Numeric Fields
DBF_CHAR, … , DBF_DOUBLE
  Standard C datatypes
  All attributes except size, extra, menu meaningful
Arrays
  dbd file must define special(SPC_DBADDR)
  Record support must implement cvt_dbaddr, get_array_info, put_array_info
  No support by Database Configuration Tools.

## Slide 13: DBD: Enumerated Field
DBF_ENUM
  Record Support provides choices and index
  See biRecord, mbbiRecord, etc
  Actual field type is unsigned short
  Record support MUST implement
    get_enum_str
    put_enum_str
    get_enum_strs

## Slide 14: DBD Menu Field
DBF_MENU
  menu(<menuname>) {
  choice(<choicename>,”<choicevalue>“)
  …
  }
  …
  recordtype(<recordtype>) {
  field(<fieldname>,DBF_MENU) {
  menu(<menuname>) }

## Slide 15: Menu Field Example
Example
  menu(menuYesNo) {
  choice(menuYesNo,”NO”)
  choice(menuYesNo,”YES”)
  }
  …
  field(PINI,DBF_MENU) {
  …
  menu(menuYesNo)
  }

## Slide 16: DBD Device Field
DBF_DEVICE
  Database Common Field - DTYP
  Related to device definitions
  Has associated INP or OUT field
  Device Support must be provided
Example field(DTYP,”Soft Channel”)
This requires a device definition like: device(ai,CONSTANT,devAiSoft,”Soft Channel”)

## Slide 17: DBD link Fields
DBF_INLINK, DBF_OUTLINK
  Not INP or OUT
    Constant link - Just initialization
    PV_LINK becomes DB_LINK or CA_LINK
  INP or OUT and Device Support
    device definitions determine choices
    Associated with choice is bus type
    Gory details in link.h. Used by device support.
DBF_FWDLINK
  references another record which is processed if it is passive.
  FLNK
    In dbCommon
    record support calls recGblFwdLink
  Other DBF_FWDLINKs can be defined
    Call dbScanFwdLink NOT recGblFwdLink

## Slide 18: Implementation: Generate include files
Generate <menu>.h and <recordtype>.h include file
dbToMenuH generates <menu>.h
  Code should use generated files instead of hard coding choices
    Many standard records written before dbToMenuH existed.
  Example menuYesNo.h
    typedef enum {
    menuYesNoNO,
    menuYesNoYES
    } menuYesNo;

## Slide 19: Generate Include Files continued
dbToRecordTypeH generates <recordtype>.h
  Code MUST use generated files
  Include code to compute field sizes, offsets
    typedef struct aiRecord {
    char name[29];
    …
    }
    #define aiRecordNAME 0
    …
    #ifdef GEN_SIZE_OFFSET
    int aiRecordSizeOffset(dbRecordType *p)
    { … }
  Only record support and associated device support is allowed to use the include files.

## Slide 20: Implementation: Record Support Module
Provide Execution Semantics
Defined via RSET - Record Support Entry Table
  /* Create RSET - Record Support Entry Table
  #define report NULL
  #define initialize NULL
  static long init_record();
  static long process();
  …
  struct rset <recordtype>RSET = {
  RSETNUMBER,
  report,
  initialize,
  init_record,
  process,
  …
  };

## Slide 21: Record Support Methods - Summary
Report, Initialization, Processing
  report
  initialize
  init_record
  process

## Slide 22: Record Support Methods - Summary
Support for Channel/ Database Access
  special
  cvt_dbaddr
  get_array_info
  put_array_info
  get_units
  get_precision
  get_enum_str
  put_enum_str
  get_enum_strs
  get_graphic_double
  get_control_double
  get_alarm_double

## Slide 23: Record Support Method: Syntax
RSET – Record Support Entry Table
  Except for RSETNUMBER just a structure of function pointers.
  Similar to JAVA interface or pure virtual C++ class
  BUT defined before standard C was available for EPICS
  Does NOT use C function prototypes
  Sorry!!!!
  Perhaps this will change in EPICS version 4.

## Slide 24: Methods: Report, Initialization, Processing
report(void *precord)
  Nothing calls this. Normally not implemented
initialize(void)
  Called once before first call to init_record .Not normally needed
init_record(void *precord,int pass)
  Normally implemented
  Called twice
    pass 0 - Can do anything except access other records. For example storage for arrays should be allocated during pass 0.
    pass 1 - Finish initialization and also call associated device support initialization
process
  VERY IMPORTANT
  Implements record semantics

## Slide 25: init_record example
/* assume val is double *val */
typedef struct xxxdset {
long number,
…
DEVSUPFUN init_record;
…
DEVSUPFUN read;
} xxxdset;
static long init_record(void *prec, int pass)
{
xxxarrayRecord *paf = (xxxarrayRecord *)prec;
xxxdest *pdset = (xxxdset *)paf->dset;
if(pass==0) {
if(paf->nelm<0) paf->nelm = 1;
paf->val = (double *)calloc(paf->nelm,sizeof(double));
return(0);
}
/* Must have dset defined */
if(!pdset !! (pdset->number< 5) || !pdest->read ) {
epicsPrintf(“%s no or invalid dset\n”,paf->name);
return(0);
}
(*pdset->init_record)(paf);
return(0);
}

## Slide 26: process overview
dbAccess:dbProcess calls process if
  Decision was made to process the record
  Record not active (PACT FALSE)
  Record is enabled (DISV !=DISA)
process with device support must
  set record active (PACT TRUE)
  Perform I/O
  Check for record specific alarms
  Raise database monitors
  Request processing of forward links
  Set PACT FALSE and return

## Slide 27: process overview continued
For asynchronous devices.
  Asynchronous start
    Initiate I/O.
    Determine a method for calling process when operation completes
    Return leaving PACT TRUE.
  Asynchronous completion
    Call process as follows: dbScanLock(precord); *(prset->process)(precord); dbScanUnlock(precord);
    process completes record processing
      Complete I/O
      Check for record specific alarms
      Raise database monitors
      Request processing of forward links
      Set PACT FALSE
      return

## Slide 28: process example
static long process(void *prec, int pass)
{
xxxarrayRecord *paf = (xxxarrayRecord *)prec;
xxxdest *pdset = (xxxdset *)paf->dset;
unsigned char pact = paf->pact;
unsigned short monitor_mask;
/* Must have dset defined */
if(!pdset !! (pdset->number< 5) || !pdest->read ) {
/*set pact true so process will not be called*/
paf->pact = TRUE;
return(0);
}
(*pdset->read)(paf);
/*return if beginning of asyn processing */
if(!pact && paf->pact) return(0);
paf->pact = TRUE;
alarm(paf);
/*sample monitor code */
monitor_mask = recGblResetAlarms(paf);
monitor_mask |= (DBE_LOG|DBE_VALUE)
db_post_events(paf,paf->val,monitor_mask);
recGblFwdLink(paf);
paf->pact = FALSE
return(0);
}

## Slide 29: alarm and monitors
alarms
  recGblSetSevr(void *prec, <alarm_status>,<alarm_severity>)
  Status and severity values defined in alarm.h
  Must prevent alarm storms on numeric values
    value fluctuating around alarm limit
    See Application Developer’s guide for algorithm
  process must call recGblResetAlarms after all alarms have been raised and before calling recGblFwdLink. Also, if possible, before raising monitors.
monitors
  db_post_event(void *prec,void *pfield, monitor_mask)
  Call for all fields that change as a result of record processing
  Support value change hysteresis when possible.
  Look at aiRecord for an example

## Slide 30: Routines with a DBADDR argument
Called by database/channel access
Call dbGetFieldIndex to find out which field.
  int fieldIndex;
  fieldIndex = dbGetFieldIndex(pdbaddr);
  if(fieldIndex == aiRecordVAL) ...
DBADDR
typedef struct dbAddr{
dbCommon *precord;
void *pfield;
void *pfldDes;
void *asPvt;
long no_elements;
short field_type;
short field_size;
short special;
short dbr_field_type;
}DBADDR;

## Slide 31: Record Support Routines - Cont.
special(DBADDR *pdbaddr,int after)
  Called if special defined in dbd file
  Called before and after field is modified.
  dbGetFieldIndex(pdbaddr)
  pdbaddr->special
    The special type as defined in .dbd file. USE SPC_MOD.
    Must include file special.h
cvt_dbaddr(DBADDR *pdbaddr)
  Called by database library when DB or CA connects to field.
  Called if special(SPC_DBADDR) specified
  Following fields of DBADDR can be changed
    no_elements
    field_type
    field_size
    special
    dbr_type

## Slide 32: Record Support Routines - Cont.
Array Routines
  Called if cvt_dbaddr sets no_elements > 1
  get_array_info(DBADDR *pdbaddr, long *no_elements, long *offset)
    Called when database access gets an array
    Must set no_elements
    Can set offset if field is circular buffer
  put_array_info( DBADDR *pdbaddr,long nNew) Called after database access has written array

## Slide 33: Record Support Routines - Cont.
Units/Precision
  get_units(DBADDR *pdbaddr, char *punits) CA has MAX_UNITS_SIZE 8
  get_precision(DBADDR *pdbaddr, long *precision) Problems with only precision.
Enumerated Values
  get_enum_str(DBADDR *pdbaddr,char *p)
  put_enum_str(DBADDR *pdbaddr,char *p)
  get_enum_strs(DBADDR *pdbaddr,dbr_enumStrs *p) CA has limit of 16 choices, 26 characters in each choice
Graphic/ Control/ Alarm Limits
  get_graphic_double(DBADDR *pdbaddr,struct dbr_grDouble *p)
  get_control_double(DBADDR *pdbaddr,struct dbr_ctrlDouble *p)
  get_alarm_double(DBADDR *pdbaddr,struct dbr_alDouble *p)

## Slide 34: Global Record Support Routines
All start with recGbl
Intended for record/device support but also called by other code
Reporting Errors Deprecated - Use errlogPrintf instead
Alarm Processing
  recGblSetSevr(void *precord, short newstat, short newsevr)
  recGblResetAlarms(void *precord);
Limits
  recGblGetGraphicDouble, recGblGetControlDouble, etc.
  Defaults for fields record support doesn’t know how to handle
  Channel Access client often not happy
  Graphics, Control, Alarm limits
recGblInitConstantLink For use on link fields with a constant value. Only works on numeric values!!

## Slide 35: Global Record Support Routines continued
recGblGetTimeStamp record support should call this each time record completes processing.
recGblFwdLink Must be called with pact true and all other processing complete

## Slide 36: Database Access Routines for Record Support
When in context of process use dbGetLink, dbPutLink
Link information
  dbGetPdbAddrFromLink gets address of DBADDR.
  dbGetRset gets address of Record Support Entry table
dbIsLinkConnected Is link connected?