## Slide 1
Jim Thomas
Lawrence Berkeley National Laboratory
The STAR Heavy Flavor Tracker

## Slide 2: The STAR Detector at RHIC w/ HFT
4 layers of Si at the Vertex
Heavy Flavor
Tracker

## Slide 3
HFT
Charm Capabilities
Full topological reconstruction of open Charm
Detailed flow & RAA studies with identified charm
500 M Event samples, each fits comfortably in a 10 week Run

## Slide 4: Who, what, when, where, why & how
The Heavy Flavor Tracker provides exquisite resolution near the BP (w/10 m space points)
The HFT was designed to do the direct topological identification of open charm
SSD
IST
Pixel Detector
Beampipe
10
20
30
-30
-10
-20
0
50-150 m

## Slide 5: HFT Location in STAR
TPC Volume
Magnet
End Cap
Solenoid
OFC
Outer Field Cage
IFC
Inner Field Cage
A key feature of the STAR Heavy Flavor Tracker is that it is removable in < 1 day while stable to 20 m … this is unique!

## Slide 6: HFT Design & Specifications
SSD
IST
PXL
HFT
Detector | Radius (cm) | Hit Resolution R/ - Z (m - m) | Radiation length
SSD | 22 | 20 / 740 | 1% X0
IST | 14 | 170 / 1800 | <1.5 %X0
PIXEL | 8 | 12 / 12 | ~0.4 %X0
 | 2.5 | 12 / 12 | ~0.4% X0
SSD existing single layer detector, double side strips (electronic upgrade)
IST one layer of silicon strips along beam direction, guiding tracks from the SSD through PIXEL detector. - proven strip technology
TPC Full 2 tracking & PID behind the Si
PIXEL
10 sectors, 2 layers (3&1)
20.7 x 20.7 m pitch
360 million pixels
new monolithic active pixel sensor (MAPS) technology from Strasbourg IPHC
TPC
SSD
IST
PXL
~1mm
~300µm
~250µm
vertex
< 30µm
6

## Slide 7: Starting from the outside and working in …
Inner Detector Support (IDS) installed in STAR for Run 12
PXL engineering test w/ 3 sectors scheduled Run 13
HFT (of course) not installed but this is where it will go (note that PXL can go in later :-)
Carbon Fiber composite structures are a Core Competency of the LBNL Engineering Division  Synergy

## Slide 8: The SSD is an Existing Detector  Upgrade
Upgrade the electronics, cooling and DAQ to allow for 200 Hz  1 kHz
EE and management responsibilities at LBL, ladder board upgrade from Subatech

## Slide 9: Intermediate Silicon Tracker
Details of wire bonding
24 ladders, liquid cooling.
Prototype Ladder
S:N > 20:1
> 99.9% live channels
9
LBL Engineering Div staff members are fabricating the IST staves w/experience based on ATLAS Fab and R&D work
Lead by MIT and UIC

## Slide 10: PXL Detector Mechanical Design
Mechanical support with kinematic mounts (insertion side)
Insertion from one side
2 layers
5 sectors / half (10 sectors total)
4 ladders/sector
Aluminum conductor Ladder Flex Cable
Ladder with 10 MAPS sensors (~ 2×2 cm each)
carbon fiber sector tubes (~ 200 µm thick)
20 cm
Lead by LBL: RNC & Eng. Div.

## Slide 11: PXL Hardware for Engineering Test in Run13
Dummy ladders shown (heaters to test cooling )
The real ladders with Ultimate chips are under construction

## Slide 12: PXL Full Chain Test
Ladder(s)
RDO
Read Out Board
MTB
Mass Termination Board

## Slide 13: HFT Management

## Slide 14: Run Plan and First Physics
HFT 3 sectors in Y13: p+p 500 GeV, Au+Au 15 GeV, Au+Au 200 GeV
  Detector engineering run.
  First look at v2 and Rcp of D via charged daughters and displaced electrons
Full HFT in Y14: >10 weeks Au+Au 200 GeV and p+p 200 GeV
  v2 and Rcp of D/e with high precision. RAA of D/e.
  Correlations: e-D, e-m (note  comes via MTD detector)
  B  J/y via displaced electrons
Y15 and beyond … Au+Au 200 GeV and pp 200 GeV high statistics
  Systematic studies of v2 and RAA, centrality, path length, √S, etc…
  c baryon with sufficient statistics
  Correlations: e-D, e-m, D-Dbar, …

## Slide 15: Summary
The Heavy Flavor Tracker will open a new era of heavy flavor studies at STAR
  Topological reconstruction of open charm
  Displaced vertex resonances & displaced electron studies
Exquisite spatial resolution is possible with the PXL detector
  20.7 m pixels
  25 m pointing resolution for pions at 1 GeV/c
The project is on schedule and (under) budget
  $16M project, $8M at LBL
  CD 2/3 approval granted October 2011
  Carbon Fiber components installed for Run 12
  PXL Engineering test run scheduled for Run 13
  Early completion date: HFT installed and tested by October 2013
  Full HFT: PXL plus IST and SSD on track for Run 14
  CD4 is scheduled for July 15, 2015

## Slide 16
Backup Slides

## Slide 19: Cost Matrix
$8M of this scope takes place at LBL, currently ~$7M in-house
Contingency is still ~35% of ETC … so a very healthy project

## Slide 20
PROJECT STATUS as of Oct 9, 2012 |  | 
Project Type | MIE | 
CD-1 | Planned: Q4FY10 | Actual: 8/31/10
CD-2 | Planned: Q4FY11 | Actual: 10/11/11
CD-3 | Planned: Q4FY11 | Actual: 10/11/11
CD-4 | Planned: Q3FY15 | Actual: TBD
TPC Percent Complete | Planned: _59_% | Actual: _38__%
TPC Cost to Date | $5,307K | 
TPC Committed to Date | $6,172K | 
TPC | $16,687K (inc. 1,187 redirect) | 
TEC | $16,387K | 
Contingency Cost (w/Mgmt Reserve) | $3,458 | _50__% to go
Contingency Schedule on CD-4 | __18__months | _160_% (30 mo to go)
CPI Cumulative | N/A | 
SPI Cumulative | N/A | 

## Slide 21: Summary Schedule

## Slide 22: DCA resolution performance r-phi and z
GEANT: Realistic detector geometry + Standard STAR tracking
including the pixel pileup hits at RHIC-II luminosity
Goal with Al-based cable (Cu cable -> 55 micron at 750 MeV/c K)
22

## Slide 23: Inner Detector Support (IDS)
MSC
Pixel Insertion Tube
Pixel Support Tube
IDS
East Support Cylinder
Outer Support Cylinder
West Support Cylinder
PIT
PST
ESC
OSC
WSC
Shrouds
Middle Support Cylinder
Inner Detector Support
Carbon Fiber Structures provide support for 3 inner detector systems and FGT.
All systems are highly integrated into IDS.
Installed for run-12

## Slide 24: Inner Detector Support Installed – Sept 2012

## Slide 25: Mechanical Engineering … much is done
SSD Ladders go here
Still To Do:
Split the shroud so it is easier to install the SSD ladders
Ladder Mounts
Air in and out for SSD vacuum
Cable routing under the shroud & ESC/WSC

## Slide 26: Electronics – the heart of the SSD upgrade
DAQ – 1.4.2.3
DDL
DAQ room
Outer support cylinder
South platform VME crate
RDO (1 of 8) – 1.4.2.2
Slave
FPGA
Slave
FPGA
Slave
FPGA
Slave FPGA
Slave FPGA
Master FPGA
DAQ interface
TRG interface
VME FPGA
Fiber links
Ladder cards – 1.4.2.1
VME interface
Notes: Ladder cards: one on each end of ladder, each reads out one face of ladder
Fiber links connect ladders to RDO
5 ladder cards – 5 ladder faces
One chip (slave FPGA) is dedicated to processing and buffering data from a single ladder
Master FPGA handles interaction with TRG and DAQ
Link to DAQ PC (DDL) is bidirectional 1.5 Gbps fiber [designed for ALICE @LHC]

## Slide 27: Physics – Run-14,15 projections
RCP=a*N10%/N(60-80)%
Assuming D0 v2 distribution from quark coalescence.
500M Au+Au m.b. events at 200 GeV.
- Charm v2
Medium thermalization degree
Drag coefficients
Assuming D0 Rcp distribution as charged hadron.
500M Au+Au m.b. events at 200 GeV.
Charm RAA
Energy loss mechanism
Color charge effect
Interaction with QCD matter

## Slide 28: Charmed baryons (Lambdac) – Run-16
c p K  Lowest mass charm baryons c = 60 m
c/D enhancement?
0.11 (pp PYTHIA)  0.4-0.9 (Di-quark correlation in QGP)
S.H. Lee etc. PRL 100, 222301 (2008)
Total charm yield in heavy ion collisions

## Slide 29: Statistics projection of eD, eB RCP & v2
Curves: H. van Hees et al. Eur. Phys. J. C61, 799(2009).
(Be) spectra obtained via the subtraction of charm decay electrons from inclusive NPEs:
- no model dependence, reduced systematic errors.
Unique opportunity for bottom e-loss and flow.
- Charm may not be heavy enough at RHIC, but how is bottom?

## Slide 30: Direct Topological Identification of Open Charm
The STAR Heavy Flavor Tracking Upgrade will identify daughters of the decay ( e.g. D0  K-++ ) and do direct topological reconstruction of open charm hadrons.
No Mixed events, no random background subtraction.
Goal: Put a high precision detector near the IP to extend the TPC tracks to small radius
50-150 m

## Slide 31: STAR Muon Tracker Detector (MTD)

## Slide 32: Quarkonium from the MTD
J/: S/B=6 in d+Au and S/B=2 in central Au+Au collisions
Excellent mass resolution: separate different upsilon states
With HFT, study BJ/ X; J/ using displaced vertices
Heavy flavor collectivity and color
screening, quarkonia production
mechanisms:
J/ RAA and v2; upsilon RAA …
Z. Xu, BNL LDRD 07-007; L. Ruan et al., Journal of Physics G: Nucl. Part. Phys. 36 (2009) 095001
32

## Slide 33: B tagged J/psi
Prompt
J/ from B
Current measurement via J/ -hadron correlation with large uncertainties.
Combine HFT+MTD in di-muon channel
  Separate secondary J/ from prompt J/ 
  Constrain the bottom production at RHIC
STAR Preliminary
Zebo Tang, NPA 00 (2010) 1.

## Slide 34: Walt Kelly’s Pogo
The HFT management team employs the latest and most sophisticated Project Management techniques.